# NasmPlus Manual
NasmPlus version 0.10
manual version 0.10
documented by: 張道遠(Kandu)
WJ
## Introduction

The NasmPlus Manual provides the information you need to write high-level assembly-language with
NasmPlus.
NasmPlus is a plus program based on NASM (The NetWide Assembler).
As you know, NASM is a wonderful multi-platform compiler, and all its fault is nonsupport of high-level decision directives. It's a hard work if you want to code a long program with only assembly-language that have no high-level decision derectives allowed. And I've been coding an OS for WJ with NASM and FPC(Free Pascal), and I need a tool to simplify low-level developing, so I coded NasmPlus. Thus, it's also a present for WJ.
NasmPlus is based on NASM. NasmPlus calls NASM to do the real work. Please install NASM first. And this manual gives no description that should be described in NASM manual. Better read the NASM manual first.

### Document Conventions
The following document conventions are used throughout this manual:

Example Description

KEY TERMS Bold type indicates text that must be typed exactly as shown.
        This includes assembly-language instructions, directives,
        symbols, operators, and keywords in other languages.
Placeholders Italics indicate variable information supplied by the user.
[argument] Items inside square brackets are optional.
{register|memory} Braces and a vertical bar indicate a choice between two or more
        items. You must choose one of the items unless square brackets
        surround the braces.

## SYNOPSIS

NasmPlus { filename [ -@ response file ] [ -f format ] [ -o outfile ] [ -l listfile ] [ options... ] | -v | -h }
Note: NASM and NasmPlus are the same but NasmPlus always takes the first parameter as filename.

## Controlling Program Flow

### #if
Syntax:
        #if condition
        [statements]
        [#else
        [statements]]
        #end
Example:
        #if #>(eax,3)
        dec eax
        #else
        inc eax
        #end

generates this code:

cmp eax, 3
jb labelbyap_2
dec eax
jmp labelbyap_1
labelbyap_2:
inc eax
labelbyap_1:

If eax greater than 3 then decrement eax, else increment eax.

### #while
Syntax:
        #while condition
        [statements]
        #end
Example:
        #while #or(#>(eax,3),z?)
        cld
        #end

generates this code:

labelbyap_2:
cmp eax, 3
jbe labelbyap_3
jmp labelbyap_4
labelbyap_3:
jnz labelbyap_1
labelbyap_4:
cld
jmp labelbyap_2
labelbyap_1:

While eax great than 3 or bit zf in flag register is seted then cld.

### #repeat
Syntax:
        #repeat
        [statements]
        #until condition
Example:
        #repeat
        movsb
        #until #=(byte [esi],0)
generates this code:
labelbyap_1:
movsb
cmp byte[esi], 0
jnz labelbyap_1

Copy chars until the null-terminated. It is used to copy a null-terminated string.

Some more complex examples:

        #if #and(#z?,#s<([SomeData],ax))
        #while #<(ax,3)
        inc ax
        #end
        #else
        #repeat
        mov eax,[esi]
        mov [edi],eax
        cmp eax,0
        #until #z?
        #end
        jmp continue
        SomeData dw 0
        continue:
        *** ***

generates this code:

jnz labelbyap_2
cmp [SomeData], ax
jge labelbyap_2
labelbyap_4:
cmp ax, 3
jae labelbyap_3
inc ax
jmp labelbyap_4
labelbyap_3:
jmp labelbyap_1
labelbyap_2:
labelbyap_5:
mov eax,[esi]
mov [edi],eax
cmp eax,0
jnz labelbyap_5
labelbyap_1:
jmp continue
SomeData dw 0
continue:

## Condition List

#z?
#e?
#nz?
#ne?
#s?
#ns?
#o?
#no?
#p?
#pe?
#np?
#po?
#b?
#nae?
#c?
#nb?
#ae?
#nc?
#be?
#na?
#nbe?
#a?
#l?
#nge?
#nl?
#ge?
#le?
#ng?
#nle?
#g?
#and(sub condition1,sub condition2)
#or(sub condition1,sub condition2)
#not(sub condition)
#be(sub condition)
#>(sub condition1,sub condition2)
#<=(sub condition1,sub condition2)
#s>(sub condition1,sub condition2)
#s<=(sub condition1,sub condition2)
#>=(sub condition1,sub condition2)
#<(sub condition1,sub condition2)
#s>=(sub condition1,sub condition2)
#s<(sub condition1,sub condition2)
#=(sub condition1,sub condition2)
#<>(sub condition1,sub condition2)

The different between #>() and #s>() is: the data inside #s>() is treated as signed number, the one inside #>() is treated as unsigned number. So are the other conditions. E.g #s>(eax,3) generates jle **, and #>(eax,3) generates jbe **.
#be(condition) is equal to #not(#not(condition)).